ECE 3337 – Lab Report 1
BJT Amplifiers
Arnav Goyal (251244778)

# Prelaboratory Preparation
Only final results for each question are shown here, complete work can be found at the end of this report.
## Common-Emitter Amplifier
### 1.1
N/A
### 1.2
DC Biasing the CE Amplifier as noted in the question gives the following resistor values
Resistor	Expression	Numerical Value [ %OMEGA ]	Std Lab Value [ %OMEGA ]
R_1	{ V_cc - V_B } over {10 cdot i_B }	33.200 k	33.000 k
R_2	V_B over { 10 cdot i_B }	6.800 k	6.800 k
R_C	{V_cc - V_C} over { i_C}	800	820
R_E	V_E over i_E	199	200

### 1.3
After Small Signal AC Analysis the following was found for the input/output resistances and voltage/current gains.
Note: All Output resistances are calculated such that we are not considering the load-resistance R_L

Value	Expression	Numerical Value
R_inp	R_1 parallel R_2 parallel r_%pi	849 [ %OMEGA ]
R_out	R_C	800 [ %OMEGA ]
A_v	- g_m (R_C parallel R_L)	-132.765 [V/V]
A_i	A_V cdot {R_inp over R_L}	-28.902 [A/A]

### 1.4
Schematic 1, shows the Microcap simulation with standard resistors, and DC bias point results of the BJT with %beta = 200 .

Schematic 1: DC Simulation of the Common-Emitter Amplifier
### 1.5
Plot 1 shows the Transient Analysis for a 1 kHz sine wave with 20mV amplitude.
Note: The plot in red is the load voltage, and the plot in blue is the AC source voltage

Plot 1: Transient Simulation of the Common-Emitter Amplifier with a 20 mV 1kHz sine input

## Common-Collector Amplifier
### 2.1
DC Biasing the CC Amplifier as noted in the question gives the following resistor values
Resistor	Expression	Numerical Value [ %OMEGA ]	Std Lab Value [ %OMEGA ]
R_1	{ V_cc - V_B } over {10 cdot i_B }	17.200k	18.000k
R_2	V_B over { 10 cdot i_B }	22.800k	22.000k
R_E	V_E over i_E	995	1.000k

### 2.2
After Small Signal AC Analysis the following was found for the input/output resistances and voltage/current gains.
Note: All Output resistances are calculated such that we are not considering the load-resistance R_L

Value	Expression	Numerical Value
R_inp	[R_1 parallel R_2] parallel [r_%pi + (1+%beta)(R_E parallel R_L)]	9.324k [ %OMEGA ]
R_out	R_E parallel {r_%pi + R_1 parallel R_2} over {1 + %beta}	51.42 [ %OMEGA ]
A_v	{[g_m + {1 over r_%pi}](R_E parallel R_L)} over {1 + [g_m + {1 over r_%pi}](R_E parallel R_L)}	0.9937 [V/V]
A_i	A_V cdot {R_inp over R_L}	180.199 [A/A]

### 2.3
Schematic 2 shows the DC operating point of the Common-Collector amplifier with %beta = 200 .

Schematic 2: DC Simulation of the Common-Collector Amplifier

### 2.4
Plot 2 shows the Transient Analysis for a 1 kHz sine wave with 20mV amplitude.
Note: The plot in red is the load voltage, and the plot in blue is the AC source voltage

Plot 2: Transient Simulation of the Common-Collector Amplifier with a 0.2 V 1kHz sine input
# Procedure

Micro-Cap Simulation	Lab Measurements
f [Hz] V_inp [V] V_out [V] A_v [dB] / 50 20m 200.90m / 100 20m 371.71m / 200 20m 675.94m / 500 20m 1.19 / 1k 20m 1.41 / 10k 20m 1.52 / 20k 20m 1.52 / 100k 20m 1.52	V_inp [V] V_out [V] A_v [dB]

Table 1: Common-Emitter Amplifier Frequency Response
Micro-Cap Simulation	Lab Measurements
f [Hz] V_inp [V] V_out [V] A_v [dB] / 50 200m 197.903m / 100 200m 197.929m / 200 200m 197.936m / 500 200m 197.938m / 1k 200m 197.938m / 10k 200m 197.938m / 20k 200m 197.938m / 100k 200m 197.938m	V_inp [V] V_out [V] A_v [dB]

Table 2: Common-Collector Amplifier Frequency Response