ECE 3337 – Lab Report 1
BJT Amplifiers
Arnav Goyal (251244778)

# Objectives
1. To determine quiescent point of a common emitter and common collector amplifiers and calculate the values of the resistors Rc, Re, R1 and R2. .
2. To simulate and measure CE and CC amplifier gain at different frequencies using MicroCap software.
# Prelaboratory Preparation
Only final results for each question are shown here, complete work can be found in screenshots at the end of this report under the Prelab Work section.
## Common-Emitter Amplifier
### 1.1
N/A
### 1.2
DC Biasing the CE Amplifier as noted in the question gives the following resistor values
Resistor	Expression	Numerical Value [ %OMEGA ]	Std Lab Value [ %OMEGA ]
R_1	{ V_cc - V_B } over {10 cdot i_B }	33.200 k	33.000 k
R_2	V_B over { 10 cdot i_B }	6.800 k	6.800 k
R_C	{V_cc - V_C} over { i_C}	800	820
R_E	V_E over i_E	199	200

### 1.3
After Small Signal AC Analysis the following was found for the input/output resistances and voltage/current gains.
Note: All Output resistances are calculated such that we are not considering the load-resistance R_L

Value	Expression	Numerical Value
R_inp	R_1 parallel R_2 parallel r_%pi	849 [ %OMEGA ]
R_out	R_C	800 [ %OMEGA ]
A_v	- g_m (R_C parallel R_L)	-132.765 [V/V]
A_i	A_V cdot {R_inp over R_L}	-28.902 [A/A]

### 1.4
Schematic 1, shows the Microcap simulation with standard resistors, and DC bias point results of the BJT with %beta = 200 .

Schematic 1: DC Simulation of the Common-Emitter Amplifier
### 1.5
Plot 1 shows the Transient Analysis for a 1 kHz sine wave with 20mV amplitude.
Note: The plot in red is the load voltage, and the plot in blue is the AC source voltage

Plot 1: Transient Simulation of the Common-Emitter Amplifier with a 20 mV 1kHz sine input

## Common-Collector Amplifier
### 2.1
DC Biasing the CC Amplifier as noted in the question gives the following resistor values
Resistor	Expression	Numerical Value [ %OMEGA ]	Std Lab Value [ %OMEGA ]
R_1	{ V_cc - V_B } over {10 cdot i_B }	17.200k	18.000k
R_2	V_B over { 10 cdot i_B }	22.800k	22.000k
R_E	V_E over i_E	995	1.000k

### 2.2
After Small Signal AC Analysis the following was found for the input/output resistances and voltage/current gains.
Note: All Output resistances are calculated such that we are not considering the load-resistance R_L

Value	Expression	Numerical Value
R_inp	[R_1 parallel R_2] parallel [r_%pi + (1+%beta)(R_E parallel R_L)]	9.324k [ %OMEGA ]
R_out	R_E parallel {r_%pi + R_1 parallel R_2} over {1 + %beta}	51.42 [ %OMEGA ]
A_v	{[g_m + {1 over r_%pi}](R_E parallel R_L)} over {1 + [g_m + {1 over r_%pi}](R_E parallel R_L)}	0.9937 [V/V]
A_i	A_V cdot {R_inp over R_L}	180.199 [A/A]

### 2.3
Schematic 2 shows the DC operating point of the Common-Collector amplifier with %beta = 200 .

Schematic 2: DC Simulation of the Common-Collector Amplifier

### 2.4
Plot 2 shows the Transient Analysis for a 1 kHz sine wave with 20mV amplitude.
Note: The plot in red is the load voltage, and the plot in blue is the AC source voltage

Plot 2: Transient Simulation of the Common-Collector Amplifier with a 0.2 V 1kHz sine input
# Procedure

### 1.1 – N/A
### 1.2 – N/A
### 1.3 – N/A
### 1.4 – N/A
### 1.5, 1.6, 1.7
See Table 1 for Enumerated Values.
During the lab the oscilloscopes were not working, the drawings cannot be done as I had to take the values of someone else.

Micro-Cap Simulation	Lab Measurements
f [Hz] V_inp [V] V_out [V] A_v [dB] / 50 20m 197.8m 19.904 / 100 20m 371.7m 25.384 / 200 20m 678.9m 30.616 / 500 20m 1.19 35.457 / 1k 20m 1.41 36.973 / 10k 20m 1.52 37.618 / 20k 20m 1.52 37.618 / 100k 20m 1.52 37.618	V_inp [V] V_out [V] A_v [dB] / 23.6m 202m 18.65 / 24m 380m 23.99 / 23.6m 690m 29.32 / 23.6m 1.28 34.68 / 23.6m 1.62 36.73 / 22.4m 1.82 38.19 / 22.4m 1.82 38.19 / 22.4m 1.82 38.19

Table 1: Common-Emitter Amplifier Frequency Response

### 1.8
The Frequency Response of the Common-Emitter (CE) amplifer meets expectations, it has a low gain at low frequencies due to the decoupling capacitors, and the midband gain is relatively stable, I do not think we see the high-frequency behaviour in the tables above as the max frequency is relatively low at around 100kHz. These observations also align with the Micro-Cap simulations within the degree of reasonable error.

### 1.9
Without access to a working oscilloscope I can only approximate these values. The Supply voltage sets an approximation of the maximum output voltage of the CE amplifier, so around 10V. The corresponding input for this 10V output wave would be dependent on the gain, supposing the input signal was used at 1kHz, we observe a dB gain of 36.967 dB, we can use this to approximate the input voltage as 141.8 mV.
### 1.10
The CE Amplifier is an inverting amplifier, as it has a phase-shift of approximately 180. This is because the current flows upwards from ground and through the load resistor during the positive sweep of the input (causing a voltage drop), and the inverse happens during the negative sweep of the signal (causing a voltage gain).

### 2.1 - N/A
### 2.2 – N/A
### 2.3 – N/A
### 2.4
See Table 2
### 2.5
During the lab the oscilloscopes were not working, the drawings cannot be done as I had to take the values of someone else.
### 2.6
The Common-Collector (CC) amplifier is essentially a voltage-buffer, but current gain amplifier, this is evident due to the constant-voltage gain of about 0dB from Table 2.
### 2.7
Once again, without access to working oscilloscopes I can only estimate this value. Here since the voltage is buffered (approx 0 gain) we can assume clipping appears at the output when there is an input of > 10V on the input.

### 2.8
The CC Amplifier is a voltage buffer, this means it is a non-inverting amplifier.

Micro-Cap Simulation	Lab Measurements
f [Hz] V_inp [V] V_out [V] A_v [dB] / 50 200m 197.903m -0.0916 / 100 200m 197.929m -0.0939 / 200 200m 197.936m -0.0901 / 500 200m 197.938m -0.0902 / 1k 200m 197.938m -0.0901 / 10k 200m 197.938m -0.0901 / 20k 200m 197.938m -0.0901 / 100k 200m 197.938m -0.0901	V_inp [V] V_out [V] A_v [dB] / 212m 208m -0.1655 / 216m 216m 0 / 212m 216m 0.1624 / 212m 216m 0.1624 / 212m 216m 0.1624 / 212m 216m 0.1624 / 212m 216m 0.1624 / 212m 216m 0.1624

Table 2: Common-Collector Amplifier Frequency Response

Questions

1. Do your experimental results agree with the MicroCap simulation? Comment on both the DC and the AC values. Explain any discrepancies.
Yes, the real-life and Micro-Cap simulated results align quite well and are within the 10% boundary. This holds true for both the DC Biasing values, as well as the AC values recorded in Tables 1 and 2.

2. What will the voltage gain of your CE amplifier be if RL=8𝛺 (input resistance of a speaker)?
We can use the derived formula from the table under the prelab section and sub in the proper values.
- g_m (R_C parallel R_L)
Here the values for the small-signal trans-conductance, and collector resistance are 0.2 S and 800 Ohms. This gives a -1.584 V/V Gain or approx 4dB magnitude gain.

3. Is your CE amplifier suitable for an audio amplifier?
After googling it, Most consumer-grade audio amps can provide gains of 20 to 30 dB, our CE’s 4dB gain is very small in comparison. So no this would not be suitable as an audio amplifier.

4. What is the main purpose of using the emitter follower?
As discussed previously, the emitter follower (or CC amp) can be used as a voltage-buffer with current gains. This can be useful to impedance match (isolate) different sub-blocks within a complex analog circuit design. As the input and output are not directly connected, but are essentially coupled through a transistor.

# Prelab Work
This section holds the screenshots of the manual work done for the prelab